SECTION 16141

TABLE BOXES FOR ELECTRICAL SYSTEMS

GENERAL

CONDITIONS AND REQUIREMENTS

The General Conditions, Supplementary Conditions, and Division 1 – General Requirements apply.

SECTION INCLUDES

Table boxes for power, communications and A/V connectivity.

Cable retractors.

Under table cable management kit.

Transition channel.

RELATED SECTIONS

Specifier Note:  In this article, specify work specified in other sections that is related to work of this section.

Section 07841 - Penetration Firestopping Devices.

Section 13700 - Security Access and Surveillance:  Security systems and components.

Division 16 - Electrical:  Electrical systems and components.

Section 16700 - Communications:  Communications and audio-video systems and components.

Specifier Note:  The following paragraph is a sample that may be used in this article.  Add to or delete from the following as appropriate for the specific project.

Section [xxxxx] – [Section Title]:  [Include brief description of work specified in another section that is related to the work of this section.]

SUBMITTALS

Specifier Note:  In this article, specify various types of data to be furnished by the contractor before, during, or after construction. Topics included in this article are:  product data, shop drawings, samples, design data, test reports, certificates, manufacturers’ instructions, manufacturers’ field reports, qualification statements, and closeout submittals.

Submit under provisions of Section [01330] [______].

Product Data:  Submit for table boxes, cable retractors, under table cable management, and transition channel.

Samples:  Submit [three (3)] [___________] with required color and finish.  Show standard color ranges available.

QUALITY ASSURANCE

Specifier Note:  In this article, describe qualifications, regulatory requirements, certifications, field samples, mock-ups, and pre-installation meetings.

Manufacturer Qualifications:  Firms regularly engaged in manufacture of electrical table boxes, fittings, cable retractors, under table cable management, and transition channel of the types and sizes required, whose products have been in satisfactory use in similar service for not less than 10 years.  Provide electrical table boxes, fittings, cable retractors, under table cable management kit, and transition channel produced by a manufacturer listed in this section.

Source Limitations:  Obtain each type of table box, fitting, cable retractor, under table cable management kit, and transition channel through one (1) source from a single manufacturer.

Electrical Boxes and Fittings:  Comply with requirements of applicable local codes, NEC, UL, ETL, and NEMA Standards pertaining to boxes and fittings.

DELIVERY, STORAGE AND HANDLING

Deliver table boxes, fittings, cable retractors, under table cable management kits, and transition channels in factory labeled packages.

Store and handle in strict compliance with manufacturer’s written instructions and recommendations.

Protect from damage due to weather, excessive temperature, and construction operations.

PRODUCTS

MANUFACTURERS

Basis-of-Design Product:  The design for table boxes, fittings, cable retractors, under table cable management kits, and transition channels is based on InteGreat™ products manufactured by Legrand/Wiremold, 60 Woodlawn Street, West Hartford, CT 06110; toll-free 800-621-0049, telephone 860-233-6251, fax 860-232-2062; Web Site: www.legrand.us/wiremold.

Substitutions will be considered under provisions of Section 01635.

TABLE BOXES

Classification and Use:  Table boxes shall be cETLus listed furniture power distribution units.

Table Boxes, General:  InteGreat™ A/V Table Boxes shall provide convenience outlets for power, data and A/V services.

Table Boxes are designed to fit together with other InteGreat™ products providing cable protection and organization.

Specifier Note: Retain one option in the following paragraph; the first one for a black finish or the second one for an aluminum finish.

Table Boxes:  InteGreat™ A/V Table Boxes Catalog No [TB672APBK] [TB672APAL].

Cover:  Brushed, anodized aluminum cover in [a black] [an aluminum] finish with beveled edges and “soft-touch” handle.

Cover contains a “pocket” door which fully recesses into the box when open, giving access to connections without obstructing work surface.  A finishing plate hides hardware on activation surface and permits labeling of the AVIP plates.

Cover flange allows for 1/4-inch [6.4mm] of forgiveness in the cut out opening.

Activation Surface:  Adjustable downward in 1/2-inch [12.7mm] increments, from one (1) inch to four (4) inches [25mm to 102mm] to allow cover to close even when large style connectors are used.

Provide table boxes with a 12 foot SJT cord for easy connection to electrical infrastructure.

Supply tables boxes with a cable grommet kit that can accommodate up to eight (8) pull out connections.  Boxes shall also be capable of accepting up to five (5) Wiremold AVIP or Extron® MAAP connectors.

Provide table boxes with two (2) 15 amp receptacles in top compartment and one (1) 15 amp receptacle on underside of box.

CABLE RETRACTORS

Cable Retractors:  InteGreat™ Series cable retractors; mounts directly to InteGreat™ Series A/V Table Box or underside of conference room table using a horizontal mounting bracket.

Cable Retractors with Category 6 Cable:  Catalog No. TBCRCAT6; loaded with 12 feet [3.66m] of Cat6 cable that extends out five (5) feet [1.52m] from retractor.  Supply retractor with a female input from building infrastructure and a male connector on the output side.

Cable Retractors with VGA Cable:  Catalog No. TBCRVGA; loaded with 12 feet [3.66m] of VGA cable that extends out five (5) feet [1.52m] from retractor.  Supply retractor with a female input from building infrastructure and a male connector on the output side.

Cable Retractors with HDMI Cable:  Catalog No. TBCRHDMI; loaded with 12 feet [3.66m] of HDMI cable that extends out five (5) feet [1.52m] from retractor.  Supply retractor with a female input from building infrastructure and a male connector on the output side.  Provide input side with mounting tab that allows installer to cable tie HDMI to retractor to minimize chances of loose connections.

Cable Retractors with 3.5MM Audio Cable:  Catalog No. TBCR3.5MM; loaded with 12 feet [3.66m] of audio cable that extends out five (5) feet [1.52m] from retractor.  Supply retractor with a female input from building infrastructure and a male connector on the output side.

Cable Retractor Horizontal Mounting Brackets:  Catalog No. TBCRHMK; permits retractor to mount horizontally under conference room table, enabling cable access through a table grommet.  Multiple retractors can be mounted to each other by attaching the mounting brackets to each other.

UNDER TABLE CABLE MANAGEMENT KIT

Under Table Cable Management Kit:  InteGreat™ Series under table cable management kit provides clean cable management for power, communication and A/V cables on horizontal underside of table.

Under Table Cable Management Kit:  Catalog No. UTCM5; includes five (5) feet [1.524mm] length of divided base, five (5) feet [1.524mm] length of mounting hinge rail and four (4) latching clips; black, nonmetallic construction.

TRANSITION CHANNELS

Transition Channels:  InteGreat™ Series transition channels continue cable management and protection from underside of the table to the floor, where cables can gain access to building infrastructure.  Channel fits directly into under table cable management kit on underside of table and mates with poke-thru device or over floor raceway for smooth transition to building infrastructure.

Transition Channels:  Catalog No. MRTC; consists of aluminum center spline with steel mounting plate and four (4) screws, black aluminum side channels, black nonmetallic  bottom boot and two (2) black nonmetallic transition covers.

EXECUTION

EXAMINATION

Specifier Note: Retain one (1) of the options in the first paragraph below and delete the other one.

Examine conditions under which table boxes, cable retractors, under table cable management kit, and transition channels are to be installed.  Notify the [Architect/Engineer] [Construction Manager] in writing of conditions detrimental to proper completion of the work.  Do not proceed with work until unsatisfactory conditions have been corrected.

INSTALLATION

Strictly comply with manufacturer's installation instructions and recommendations.  Coordinate installation with adjacent work to ensure proper clearances and to prevent electrical hazards.

CLEANING AND PROTECTION

Clean exposed surfaces using non-abrasive materials and methods recommended by manufacturer.

Protect products until acceptance.

END OF SECTION

A copyright license to reproduce this specification is hereby granted to non-manufacturing engineers, architects and specification writers.

|  | Legrand / Wiremold U.S. and International: 60 Woodlawn Street ( West Hartford, CT 06110 1-800-621-0049 ( FAX: 860-232-2062 ( Outside U.S.: 860-233-6251 Canada: 570 Applewood Crescent ( Vaughan, Ontario L4K 4B4 1-800-723-5175 ( FAX: 905-738-9721 |
| --- | --- |
| (2013 Legrand/Wiremold All Rights Reserved | EDXXXX – September 2013 – For latest specs visit www.wiremold.com |