SECTION 26 05 33.16

TABLE BOXES FOR ELECTRICAL SYSTEMS

GENERAL

CONDITIONS AND REQUIREMENTS

The General Conditions, Supplementary Conditions, and Division 01 – General Requirements apply.

SECTION INCLUDES

Table boxes for power and communications connectivity.

RELATED SECTIONS

Specifier Note:  In this article, specify work specified in other sections that is related to work of this section.

Division 26 - Electrical:  Electrical systems and components.

Division 27 - Communications:  Communications and audio-video systems and components.

Specifier Note:  The following paragraph is a sample that may be used in this article.  Add to or delete from the following as appropriate for the specific project.

Section [xx xx xx] – [Section Title]:  [Include brief description of work specified in another section that is related to the work of this section.]

SUBMITTALS

Specifier Note:  In this article, specify various types of data to be furnished by the contractor before, during, or after construction. Topics included in this article are:  product data, shop drawings, samples, design data, test reports, certificates, manufacturers’ instructions, manufacturers’ field reports, qualification statements, and closeout submittals.

Submit under provisions of Section [01 33 00] [______].

Product Data:  Submit for table boxes.

Samples:  Submit [three (3)] [___________] with required color and finish.  Show standard color ranges available.

QUALITY ASSURANCE

Specifier Note:  In this article, describe qualifications, regulatory requirements, certifications, field samples, mock-ups, and pre-installation meetings.

Manufacturer Qualifications:  Firms regularly engaged in manufacture of electrical table boxes and fittings of the types and sizes required, whose products have been in satisfactory use in similar service for not less than 10 years.  Provide electrical table boxes and fittings produced by a manufacturer listed in this section.

Source Limitations:  Obtain each type of table box through one (1) source from a single manufacturer.

Electrical Boxes and Fittings:  Comply with requirements of applicable local codes, NEC, UL, ETL, and NEMA Standards pertaining to boxes and fittings.

DELIVERY, STORAGE AND HANDLING

Deliver table boxes in factory labeled packages.

Store and handle in strict compliance with manufacturer’s written instructions and recommendations.

Protect from damage due to weather, excessive temperature, and construction operations.

PRODUCTS

MANUFACTURERS

Basis-of-Design Product:  The design for table boxes and fittings is based on the deQuorum™ Flip-Up Table Box manufactured by legrand/Wiremold, 60 Woodlawn Street, West Hartford, CT 06110; toll-free 800-621-0049, telephone 860-233-6251, fax 860-232-2062; Web Site: www.legrand.us/wiremold.

Substitutions will be considered under provisions of Section 01 25 00.

TABLE BOXES

Classification and Use:  Table boxes shall have been examined, tested and listed by Underwriters Laboratories Inc. (UL).

Table Boxes, General:  Multi-service table boxes shall provide convenience outlets for power and data.

Specifier Note: Retain one of the finish colors in the following paragraph and delete the other one.

Table Boxes:  deQuorum™ Flip-Up Series Table Boxes; cULus Listed Relocatable Power Tap under File No. E66421 Guide XBYS; meets Article 380 of NEC.  Service location above table; furnish with six (6) foot cord; cover color - [black] [stainless].

Table Box Units:

Catalog No. DQFP15[BK][ST]; [black] [stainless steel] finish; single flip-up unit which includes one (1) 15A black tamper-resistant duplex receptacle.  Units are supplied with a 6 foot [1.83m] cord.

Catalog No. DQFP20[BK][ST]; [black] [stainless steel] finish; single flip-up unit which includes one (1) 20A black tamper-resistant duplex receptacle.  Units are supplied with a 6 foot [1.83m] cord.

Catalog No. DQFP15U[BK][ST]; [black] [stainless steel] finish; single flip-up unit which includes one (1) 15A black tamper-resistant duplex receptacle with two (2) USB ports that provide 3.1 amps.  Units are supplied with a 6 foot [1.83m] cord.

Catalog No. DQFP20U[BK][ST]; [black] [stainless steel] finish; single flip-up unit which includes one (1) 20A black tamper-resistant duplex receptacle with two (2) USB ports that provide 3.1 amps.  Units are supplied with a 6 foot [1.83m] cord.

Catalog No. DQFP15[BK][ST]-2A; [black] [stainless steel] finish; dual flip-up unit which includes one (1) 15A black tamper-resistant duplex receptacle and one (1) opening that will accept an adapter for one (1) Wiremold CM Series Open System 2A module, one (1) Ortronics® Series II or one (1) TracJack adapter that accommodates a wide range of communication outlets.  Adapters are included.  Units are supplied with a 6 foot [1.83m] cord.

Catalog No. DQFP20[BK][ST]-2A; [black] [stainless steel] finish; dual flip-up unit which includes one (1) 20A black tamper-resistant duplex receptacle and one (1) opening that will accept an adapter for one (1) Wiremold CM Series Open System 2A module, one (1) Ortronics® Series II or one (1) TracJack adapter that accommodates a wide range of communication outlets.  Adapters are included.  Units are supplied with a 6 foot [1.83m] cord.

Catalog No. DQFP15U[BK][ST]-2A; [black] [stainless steel] finish; dual flip-up unit which includes one (1) 15A black tamper-resistant duplex receptacle with two (2) USB ports that provide 3.1 amps.  Second opening will accept adapter for one (1) Wiremold CM Series Open System 2A module, one (1) Ortronics® Series II or one (1) TracJack adapter that accommodates a wide range of communication outlets.  Adapters are included.  Units are supplied with a 6 foot [1.83m] cord.

Catalog No. DQFP20U[BK][ST]-2A; [black] [stainless steel] finish; dual flip-up unit which includes one (1) 20A black tamper-resistant duplex receptacle with two (2) USB ports that provide 3.1 amps.  Second opening will accept adapter for one (1) Wiremold CM Series Open System 2A module, one (1) Ortronics® Series II or one (1) TracJack adapter that accommodates a wide range of communication outlets.  Adapters are included.  Units are supplied with a 6 foot [1.83m] cord.

EXECUTION

EXAMINATION

Specifier Note: Retain one (1) of the options in the first paragraph below and delete the other one.

Examine conditions under which boxes and fittings are to be installed.  Notify the [Architect/Engineer] [Construction Manager] in writing of conditions detrimental to proper completion of the work.  Do not proceed with work until unsatisfactory conditions have been corrected.

INSTALLATION

Strictly comply with manufacturer's installation instructions and recommendations.  Coordinate installation with adjacent work to ensure proper clearances and to prevent electrical hazards.

CLEANING AND PROTECTION

Clean exposed surfaces using non-abrasive materials and methods recommended by manufacturer.

Protect boxes until acceptance.

END OF SECTION

A copyright license to reproduce this specification is hereby granted to non-manufacturing engineers, architects and specification writers.

|  | legrand / Wiremold U.S. and International: 60 Woodlawn Street ( West Hartford, CT 06110 1-800-621-0049 ( FAX: 860-232-2062 ( Outside U.S.: 860-233-6251 Canada: 570 Applewood Crescent ( Vaughan, Ontario L4K 4B4 1-800-723-5175 ( FAX: 905-738-9721 |
| --- | --- |
| (2015 legrand/Wiremold All Rights Reserved | EDXXXX – New March 2015 – For latest specs visit www.legrand.us/wiremold |